----- Alternating Bit Protocol --------

number of messages to simulate: 20
packet loss probability : 0.200000
packet corruption probability : 0.300000
average time between messages from sender's layer5 : 1000.000000
TRACE: 4

EVENT time: 1870.573975, type: 1, fromlayer5 entity: 0
        TOLAYER3: packet being corrupted
**** At 1870.573975 in A_output() : Sending pkt0: aaaaaaaaaaaaaaaaaaa ****

EVENT time: 1876.039062, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt

EVENT time: 1878.220703, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) NACK received.

EVENT time: 1890.573975, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. aaaaaaaaaaaaaaaaaaa
        TOLAYER3: packet being lost

EVENT time: 1910.573975, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. aaaaaaaaaaaaaaaaaaa
        TOLAYER3: packet being lost

EVENT time: 1930.573975, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. aaaaaaaaaaaaaaaaaaa

EVENT time: 1939.818481, type: 2, fromlayer3 entity: 1
**** At 1939.818481 in B_input() : Correct pkt received. pkt0 aaaaaaaaaaaaaaaaaaa ****
        TOLAYER3: packet being lost

EVENT time: 1950.573975, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. aaaaaaaaaaaaaaaaaaa

EVENT time: 1952.052368, type: 2, fromlayer3 entity: 1
**** At 1952.052368 in B_input() : Duplicate Packet received. Resending ACK for pkt0 aaaaaaaaaaaaaaaaaaa ****

EVENT time: 1957.324585, type: 2, fromlayer3 entity: 0
**** At 1957.324585 in A_input() : ACK received for pkt0: ****

EVENT time: 3512.483887, type: 1, fromlayer5 entity: 0
**** At 3512.483887 in A_output() : Sending pkt1: bbbbbbbbbbbbbbbbbbb ****

EVENT time: 3518.513428, type: 2, fromlayer3 entity: 1
**** At 3518.513428 in B_input() : Correct pkt received. pkt1 bbbbbbbbbbbbbbbbbbb ****
        TOLAYER3: packet being lost

EVENT time: 3532.483887, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. bbbbbbbbbbbbbbbbbbb
        TOLAYER3: packet being corrupted

EVENT time: 3536.547607, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt
        TOLAYER3: packet being corrupted

EVENT time: 3538.331543, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) Checksum does not match. Received ACK is corrupt

EVENT time: 3552.483887, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. bbbbbbbbbbbbbbbbbbb

EVENT time: 3556.642578, type: 2, fromlayer3 entity: 1
**** At 3556.642578 in B_input() : Duplicate Packet received. Resending ACK for pkt1 bbbbbbbbbbbbbbbbbbb ****
        TOLAYER3: packet being lost

EVENT time: 3572.483887, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. bbbbbbbbbbbbbbbbbbb
        TOLAYER3: packet being corrupted

EVENT time: 3578.321777, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt

EVENT time: 3580.197021, type: 2, fromlayer3 entity: 0
**** At 3580.197021 in A_input() : ACK received for pkt0: ****

EVENT time: 4948.687500, type: 1, fromlayer5 entity: 0
**** At 4948.687500 in A_output() : Sending pkt0: ccccccccccccccccccc ****

EVENT time: 4949.993652, type: 2, fromlayer3 entity: 1
**** At 4949.993652 in B_input() : Correct pkt received. pkt0 ccccccccccccccccccc ****
        TOLAYER3: packet being corrupted

EVENT time: 4955.572266, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) Checksum does not match. Received ACK is corrupt

EVENT time: 4961.679688, type: 1, fromlayer5 entity: 0
Packet dropped. Msg in transit

EVENT time: 4968.687500, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ccccccccccccccccccc
        TOLAYER3: packet being corrupted

EVENT time: 4970.443359, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt

EVENT time: 4973.321289, type: 2, fromlayer3 entity: 0
**** At 4973.321289 in A_input() : ACK received for pkt0: ****

EVENT time: 6690.848633, type: 1, fromlayer5 entity: 0
**** At 6690.848633 in A_output() : Sending pkt1: eeeeeeeeeeeeeeeeeee ****

EVENT time: 6697.967285, type: 2, fromlayer3 entity: 1
**** At 6697.967285 in B_input() : Correct pkt received. pkt1 eeeeeeeeeeeeeeeeeee ****

EVENT time: 6699.244629, type: 2, fromlayer3 entity: 0
**** At 6699.244629 in A_input() : ACK received for pkt0: ****

EVENT time: 8556.644531, type: 1, fromlayer5 entity: 0
        TOLAYER3: packet being corrupted
**** At 8556.644531 in A_output() : Sending pkt0: fffffffffffffffffff ****

EVENT time: 8558.916992, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt
        TOLAYER3: packet being lost

EVENT time: 8576.644531, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. fffffffffffffffffff
        TOLAYER3: packet being corrupted

EVENT time: 8578.451172, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt
        TOLAYER3: packet being lost

EVENT time: 8596.644531, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. fffffffffffffffffff

EVENT time: 8599.661133, type: 2, fromlayer3 entity: 1
**** At 8599.661133 in B_input() : Correct pkt received. pkt0 fffffffffffffffffff ****

EVENT time: 8604.415039, type: 2, fromlayer3 entity: 0
**** At 8604.415039 in A_input() : ACK received for pkt0: ****

EVENT time: 10421.403320, type: 1, fromlayer5 entity: 0
**** At 10421.403320 in A_output() : Sending pkt1: ggggggggggggggggggg ****

EVENT time: 10427.387695, type: 2, fromlayer3 entity: 1
**** At 10427.387695 in B_input() : Correct pkt received. pkt1 ggggggggggggggggggg ****
        TOLAYER3: packet being corrupted

EVENT time: 10435.250000, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) Checksum does not match. Received ACK is corrupt

EVENT time: 10441.403320, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ggggggggggggggggggg
        TOLAYER3: packet being lost

EVENT time: 10461.403320, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ggggggggggggggggggg

EVENT time: 10469.361328, type: 2, fromlayer3 entity: 1
**** At 10469.361328 in B_input() : Duplicate Packet received. Resending ACK for pkt1 ggggggggggggggggggg ****

EVENT time: 10473.753906, type: 2, fromlayer3 entity: 0
**** At 10473.753906 in A_input() : ACK received for pkt0: ****

EVENT time: 10750.820312, type: 1, fromlayer5 entity: 0
**** At 10750.820312 in A_output() : Sending pkt0: hhhhhhhhhhhhhhhhhhh ****

EVENT time: 10760.667969, type: 2, fromlayer3 entity: 1
**** At 10760.667969 in B_input() : Correct pkt received. pkt0 hhhhhhhhhhhhhhhhhhh ****

EVENT time: 10763.413086, type: 2, fromlayer3 entity: 0
**** At 10763.413086 in A_input() : ACK received for pkt0: ****

EVENT time: 11354.875000, type: 1, fromlayer5 entity: 0
**** At 11354.875000 in A_output() : Sending pkt1: iiiiiiiiiiiiiiiiiii ****

EVENT time: 11361.490234, type: 2, fromlayer3 entity: 1
**** At 11361.490234 in B_input() : Correct pkt received. pkt1 iiiiiiiiiiiiiiiiiii ****
        TOLAYER3: packet being lost

EVENT time: 11374.875000, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. iiiiiiiiiiiiiiiiiii

EVENT time: 11383.906250, type: 2, fromlayer3 entity: 1
**** At 11383.906250 in B_input() : Duplicate Packet received. Resending ACK for pkt1 iiiiiiiiiiiiiiiiiii ****
        TOLAYER3: packet being corrupted

EVENT time: 11385.419922, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) Checksum does not match. Received ACK is corrupt

EVENT time: 11394.875000, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. iiiiiiiiiiiiiiiiiii
        TOLAYER3: packet being corrupted

EVENT time: 11395.972656, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt

EVENT time: 11398.122070, type: 2, fromlayer3 entity: 0
**** At 11398.122070 in A_input() : ACK received for pkt0: ****

EVENT time: 12863.125977, type: 1, fromlayer5 entity: 0
        TOLAYER3: packet being lost
**** At 12863.125977 in A_output() : Sending pkt0: jjjjjjjjjjjjjjjjjjj ****

EVENT time: 12883.125977, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. jjjjjjjjjjjjjjjjjjj
        TOLAYER3: packet being lost

EVENT time: 12903.125977, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. jjjjjjjjjjjjjjjjjjj
        TOLAYER3: packet being lost

EVENT time: 12923.125977, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. jjjjjjjjjjjjjjjjjjj

EVENT time: 12928.373047, type: 2, fromlayer3 entity: 1
**** At 12928.373047 in B_input() : Correct pkt received. pkt0 jjjjjjjjjjjjjjjjjjj ****
        TOLAYER3: packet being corrupted

EVENT time: 12937.316406, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) Checksum does not match. Received ACK is corrupt

EVENT time: 12943.125977, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. jjjjjjjjjjjjjjjjjjj
        TOLAYER3: packet being corrupted

EVENT time: 12952.448242, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt
        TOLAYER3: packet being corrupted

EVENT time: 12955.444336, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) Checksum does not match. Received ACK is corrupt

EVENT time: 12963.125977, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. jjjjjjjjjjjjjjjjjjj
        TOLAYER3: packet being corrupted

EVENT time: 12964.275391, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt

EVENT time: 12971.843750, type: 2, fromlayer3 entity: 0
**** At 12971.843750 in A_input() : ACK received for pkt0: ****

EVENT time: 14147.789062, type: 1, fromlayer5 entity: 0
**** At 14147.789062 in A_output() : Sending pkt1: kkkkkkkkkkkkkkkkkkk ****

EVENT time: 14155.735352, type: 2, fromlayer3 entity: 1
**** At 14155.735352 in B_input() : Correct pkt received. pkt1 kkkkkkkkkkkkkkkkkkk ****

EVENT time: 14160.461914, type: 2, fromlayer3 entity: 0
**** At 14160.461914 in A_input() : ACK received for pkt0: ****

EVENT time: 14934.108398, type: 1, fromlayer5 entity: 0
**** At 14934.108398 in A_output() : Sending pkt0: lllllllllllllllllll ****

EVENT time: 14939.790039, type: 2, fromlayer3 entity: 1
**** At 14939.790039 in B_input() : Correct pkt received. pkt0 lllllllllllllllllll ****
        TOLAYER3: packet being corrupted

EVENT time: 14944.729492, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) Checksum does not match. Received ACK is corrupt

EVENT time: 14954.108398, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. lllllllllllllllllll
        TOLAYER3: packet being corrupted

EVENT time: 14960.876953, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt

EVENT time: 14964.594727, type: 2, fromlayer3 entity: 0
**** At 14964.594727 in A_input() : ACK received for pkt0: ****

EVENT time: 16740.972656, type: 1, fromlayer5 entity: 0
**** At 16740.972656 in A_output() : Sending pkt1: mmmmmmmmmmmmmmmmmmm ****

EVENT time: 16747.658203, type: 2, fromlayer3 entity: 1
**** At 16747.658203 in B_input() : Correct pkt received. pkt1 mmmmmmmmmmmmmmmmmmm ****
        TOLAYER3: packet being corrupted

EVENT time: 16753.369141, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) Checksum does not match. Received ACK is corrupt

EVENT time: 16760.972656, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. mmmmmmmmmmmmmmmmmmm

EVENT time: 16767.773438, type: 2, fromlayer3 entity: 1
**** At 16767.773438 in B_input() : Duplicate Packet received. Resending ACK for pkt1 mmmmmmmmmmmmmmmmmmm ****
        TOLAYER3: packet being lost

EVENT time: 16780.972656, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. mmmmmmmmmmmmmmmmmmm
        TOLAYER3: packet being lost

EVENT time: 16800.972656, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. mmmmmmmmmmmmmmmmmmm

EVENT time: 16807.478516, type: 2, fromlayer3 entity: 1
**** At 16807.478516 in B_input() : Duplicate Packet received. Resending ACK for pkt1 mmmmmmmmmmmmmmmmmmm ****
        TOLAYER3: packet being corrupted

EVENT time: 16808.884766, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) Checksum does not match. Received ACK is corrupt

EVENT time: 16820.972656, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. mmmmmmmmmmmmmmmmmmm
        TOLAYER3: packet being lost

EVENT time: 16840.972656, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. mmmmmmmmmmmmmmmmmmm
        TOLAYER3: packet being corrupted

EVENT time: 16850.687500, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt

EVENT time: 16853.703125, type: 2, fromlayer3 entity: 0
**** At 16853.703125 in A_input() : ACK received for pkt0: ****

EVENT time: 18563.248047, type: 1, fromlayer5 entity: 0
        TOLAYER3: packet being corrupted
**** At 18563.248047 in A_output() : Sending pkt0: nnnnnnnnnnnnnnnnnnn ****

EVENT time: 18570.433594, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt

EVENT time: 18572.296875, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) NACK received.

EVENT time: 18583.248047, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. nnnnnnnnnnnnnnnnnnn

EVENT time: 18587.373047, type: 2, fromlayer3 entity: 1
**** At 18587.373047 in B_input() : Correct pkt received. pkt0 nnnnnnnnnnnnnnnnnnn ****

EVENT time: 18597.298828, type: 2, fromlayer3 entity: 0
**** At 18597.298828 in A_input() : ACK received for pkt0: ****

EVENT time: 19077.343750, type: 1, fromlayer5 entity: 0
        TOLAYER3: packet being lost
**** At 19077.343750 in A_output() : Sending pkt1: ooooooooooooooooooo ****

EVENT time: 19097.343750, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ooooooooooooooooooo
        TOLAYER3: packet being lost

EVENT time: 19117.343750, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ooooooooooooooooooo
        TOLAYER3: packet being lost

EVENT time: 19137.343750, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ooooooooooooooooooo
        TOLAYER3: packet being corrupted

EVENT time: 19141.775391, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt
        TOLAYER3: packet being lost

EVENT time: 19157.343750, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ooooooooooooooooooo
        TOLAYER3: packet being lost

EVENT time: 19177.343750, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ooooooooooooooooooo
        TOLAYER3: packet being corrupted

EVENT time: 19178.880859, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt
        TOLAYER3: packet being corrupted

EVENT time: 19184.562500, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) Checksum does not match. Received ACK is corrupt

EVENT time: 19197.343750, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ooooooooooooooooooo
        TOLAYER3: packet being lost

EVENT time: 19217.343750, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ooooooooooooooooooo
        TOLAYER3: packet being corrupted

EVENT time: 19219.191406, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt
        TOLAYER3: packet being lost

EVENT time: 19237.343750, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ooooooooooooooooooo

EVENT time: 19246.056641, type: 2, fromlayer3 entity: 1
**** At 19246.056641 in B_input() : Correct pkt received. pkt1 ooooooooooooooooooo ****

EVENT time: 19248.183594, type: 2, fromlayer3 entity: 0
**** At 19248.183594 in A_input() : ACK received for pkt0: ****

EVENT time: 20009.070312, type: 1, fromlayer5 entity: 0
        TOLAYER3: packet being corrupted
**** At 20009.070312 in A_output() : Sending pkt0: ppppppppppppppppppp ****

EVENT time: 20016.244141, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt

EVENT time: 20022.039062, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) NACK received.

EVENT time: 20029.070312, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ppppppppppppppppppp

EVENT time: 20035.689453, type: 2, fromlayer3 entity: 1
**** At 20035.689453 in B_input() : Correct pkt received. pkt0 ppppppppppppppppppp ****
        TOLAYER3: packet being corrupted

EVENT time: 20042.845703, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) Checksum does not match. Received ACK is corrupt

EVENT time: 20049.070312, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ppppppppppppppppppp

EVENT time: 20056.789062, type: 2, fromlayer3 entity: 1
**** At 20056.789062 in B_input() : Duplicate Packet received. Resending ACK for pkt0 ppppppppppppppppppp ****

EVENT time: 20064.921875, type: 2, fromlayer3 entity: 0
**** At 20064.921875 in A_input() : ACK received for pkt0: ****

EVENT time: 20219.716797, type: 1, fromlayer5 entity: 0
**** At 20219.716797 in A_output() : Sending pkt1: qqqqqqqqqqqqqqqqqqq ****

EVENT time: 20225.462891, type: 2, fromlayer3 entity: 1
**** At 20225.462891 in B_input() : Correct pkt received. pkt1 qqqqqqqqqqqqqqqqqqq ****
        TOLAYER3: packet being corrupted

EVENT time: 20229.921875, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) Checksum does not match. Received ACK is corrupt

EVENT time: 20239.716797, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. qqqqqqqqqqqqqqqqqqq

EVENT time: 20246.378906, type: 2, fromlayer3 entity: 1
**** At 20246.378906 in B_input() : Duplicate Packet received. Resending ACK for pkt1 qqqqqqqqqqqqqqqqqqq ****
        TOLAYER3: packet being lost

EVENT time: 20259.716797, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. qqqqqqqqqqqqqqqqqqq

EVENT time: 20261.757812, type: 2, fromlayer3 entity: 1
**** At 20261.757812 in B_input() : Duplicate Packet received. Resending ACK for pkt1 qqqqqqqqqqqqqqqqqqq ****

EVENT time: 20268.595703, type: 2, fromlayer3 entity: 0
**** At 20268.595703 in A_input() : ACK received for pkt0: ****

EVENT time: 20965.769531, type: 1, fromlayer5 entity: 0
**** At 20965.769531 in A_output() : Sending pkt0: rrrrrrrrrrrrrrrrrrr ****

EVENT time: 20971.187500, type: 2, fromlayer3 entity: 1
**** At 20971.187500 in B_input() : Correct pkt received. pkt0 rrrrrrrrrrrrrrrrrrr ****
        TOLAYER3: packet being corrupted

EVENT time: 20978.642578, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) Checksum does not match. Received ACK is corrupt

EVENT time: 20985.769531, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. rrrrrrrrrrrrrrrrrrr

EVENT time: 20995.505859, type: 2, fromlayer3 entity: 1
**** At 20995.505859 in B_input() : Duplicate Packet received. Resending ACK for pkt0 rrrrrrrrrrrrrrrrrrr ****

EVENT time: 21000.855469, type: 2, fromlayer3 entity: 0
**** At 21000.855469 in A_input() : ACK received for pkt0: ****

EVENT time: 22332.048828, type: 1, fromlayer5 entity: 0
        TOLAYER3: packet being lost
**** At 22332.048828 in A_output() : Sending pkt1: sssssssssssssssssss ****

EVENT time: 22352.048828, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. sssssssssssssssssss

EVENT time: 22356.822266, type: 2, fromlayer3 entity: 1
**** At 22356.822266 in B_input() : Correct pkt received. pkt1 sssssssssssssssssss ****

EVENT time: 22360.324219, type: 2, fromlayer3 entity: 0
**** At 22360.324219 in A_input() : ACK received for pkt0: ****

EVENT time: 22433.802734, type: 1, fromlayer5 entity: 0
        TOLAYER3: packet being corrupted
**** At 22433.802734 in A_output() : Sending pkt0: ttttttttttttttttttt ****

EVENT time: 22436.982422, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt

EVENT time: 22444.955078, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) NACK received.

EVENT time: 22453.802734, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ttttttttttttttttttt
        TOLAYER3: packet being lost

EVENT time: 22473.802734, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ttttttttttttttttttt
        TOLAYER3: packet being corrupted

EVENT time: 22476.263672, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt

EVENT time: 22479.392578, type: 2, fromlayer3 entity: 0
  (Sender) (in A_input) NACK received.

EVENT time: 22493.802734, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ttttttttttttttttttt
        TOLAYER3: packet being corrupted

EVENT time: 22499.720703, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt
        TOLAYER3: packet being lost

EVENT time: 22513.802734, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ttttttttttttttttttt
        TOLAYER3: packet being corrupted

EVENT time: 22515.841797, type: 2, fromlayer3 entity: 1
(in B_input) Checksum does not match. Received packet is corrupt
        TOLAYER3: packet being lost

EVENT time: 22533.802734, type: 0, timerinterrupt entity: 0
(A_timerinterrupt) Resending .. ttttttttttttttttttt

EVENT time: 22541.406250, type: 2, fromlayer3 entity: 1
**** At 22541.406250 in B_input() : Correct pkt received. pkt0 ttttttttttttttttttt ****

EVENT time: 22542.511719, type: 2, fromlayer3 entity: 0
**** At 22542.511719 in A_input() : ACK received for pkt0: ****

 Simulator terminated at time 22542.511719
 after sending 20 msgs from layer5

A_ackReceived_count = 19
A_dropped_count = 1
A_corruptReceived_count = 13
A_timeoutOccurred_count = 45
A_nackReceived_count = 5
B_correctlyReceived_count = 19
B_corruptReceived_count = 20
B_duplicateReceived_count = 10